## Slide 1
ADCS:
Arduino & Simulink

## Slide 2
Requirements
Determination
Control
Determine direction of a unique light source
Need to show the light incident angle in an LCD screen. At least in the -plane
Orient the satellite’s X+/X- faces to a dynamic light source
  Minimise time to achieve orientation
  Maximise precision
Control should be a 2nd mode of operation, activated by the push of a button
Avoid oscillations
Minimise components, cabling….
The design of a control law and a complete Simulink model is encouraged
Use a filter to improve the stability of the measurement

## Slide 3
Photoresistors
  How many?
Components and Design
Need to determine the light incident angle at all times  this drives decision for n. photoresistors
Control only in -plane?
What about the structure? + need to 3d print it + needs to be light
Components
Design
Battery
Servo motor
LCD screen

## Slide 4
Circuit
Photoresistors
Servo motor
Algo así….
Hay que pensar el n de resistors…

## Slide 5
Photoresistors
Model
Dependent parameters:
  Sun incidence angle
  Intensity
    Dependent on distance
    Dependent on light source (cte.)
R = f(, I)
Source: Some_Simple_Experiments_in_Optics_Using_a_PhotoRes

## Slide 6
Servo motor
Model
The angle of rotation (0-180 degrees) depends on the input voltage to the servo motor
Include turn velocity in the model. How?
Translate angle into body axis.  Use quaternions? Tbf the angle will only be in the -plane if 1 servomotor is used.  Should we use 2 servos?
 = f(V)

## Slide 7
Structure
Photoresistors
Needs to turn 180 degrees to face the light
Needs to determine the light incidence angle in at least -plane. Preferably in 3 axis.
Requirements
Need to have holes for the photoresistors, and these need to be held by it without moving
The structure needs to be light enough for the servomotor to be able to move it
Also…

## Slide 8
Control Law
PID? Or PD to make it simpler

## Slide 9
Programming options
Program everything in Simulink?
  Pros: works for sure
  Cons: I hate simulink
Program the control law in Simulink and the rest in Arduino (C++), include the control law as a void control{} or something….
  Pros: can use the Arduino libraries. i.e. servo library  allows to get the turn angle very easily
  Cons: need to combine the code generated by Simulink with our own code. Could be problematic
Program everything in Arduino <- NO!

## Slide 10
Simulink
This should work (if the PID is properly tuned), but it is not taking into consideration a model for the servo
The servomotor should be modelled instead of using the built in functions. This could be achieved by sending a specific voltage signal to the digital pin to which the servo motor is connected to.